## Slide 1
FROM BRICKS TO PRINTS
A Classroom-to-Competition 3D Printing Workflow for Robotics Education
Roger Clement • KIPR Robotics Education

## Slide 2
The Workflow, End to End
Six stages, repeated every time a part changes
1. Build in LEGO
→
2. Model in SolidWorks
→
3. Assemble
→
4. Slice
→
5. Print & Review
→
6. Iterate
Physical craft feeds digital precision — and the loop closes every revision.
2

## Slide 3
Why We Start With LEGO, Not CAD
Zero-friction iteration
Students test fit, clearance, and balance in seconds — no software, no waiting on a render.
Everyone can contribute
A team member who has never opened a CAD package can still push, pull, and reposition bricks.
Constraints surface early
Wheelbase, sensor placement, and Wombat clearance reveal problems before a single digital line is drawn.
A physical reference for CAD
The finished brick build becomes the literal blueprint the model must match — not a guess.
3

## Slide 4
Today's Running Example
A Robot Chassis Built to Carry the KIPR Wombat
We'll follow one part — a mounting chassis for the Wombat controller — from its first LEGO mock-up through SolidWorks, slicing, and two rounds of team revision. You'll see the same physical unit at every table in the room.
4

## Slide 5
1
Building With Actual LEGO
Start from the Wombat's real footprint and mounting-hole spacing — measure it, don't estimate it.
Build the chassis deck first, then layer on standoffs and side rails to hold the controller square.
Test the assembly by hand: does it clear the drive gears? Can a cable still reach the ports?
Photograph the final brick build from four angles — this becomes the CAD reference sheet.
Keep it modular: a brick sub-assembly that fails review is rebuilt in minutes, not redrawn from scratch.
Rule of thumb
If two students can't agree on the fit by eye, it isn't ready for CAD yet.
5

## Slide 6
2
Modeling in SolidWorks
The brick build sets the dimensions. SolidWorks turns them into a part that can be measured, toleranced, and printed.
1
Reference sketch
Photos and brick measurements become the base sketch on the front plane.
2
Solid features
Extrude the deck, cut mounting holes to the Wombat's real bolt pattern, add standoffs.
3
Design intent
Fillets and wall thickness follow print-friendly rules, not just LEGO proportions.
Why not model from scratch?
Because the LEGO build already answers the hard questions — fit, clearance, orientation — before a single SolidWorks feature exists.
6

## Slide 7
2
Importing LEGO Geometry From Team Home Base
Rather than redraw every stud and axle hole, we bring in the official STL files KIPR publishes on Team Home Base and build around them.
Download the STL for the exact brick or beam already used in the physical build.
Import as a solid body in SolidWorks — treat it as reference geometry, not something to edit.
Sketch and extrude new custom features (mounts, walls, standoffs) that mate directly to the imported part.
Keep imported and custom bodies in separate features so the model stays easy to troubleshoot.
Why it matters for competition
Botball and JBC rules require an STL for any printed part, and officially released Team Home Base geometry is already vetted against the kit — starting there keeps dimensions honest and documentation painless.
Tip: attribute any prior-year STL you reuse, and resubmit it during documentation.
7

## Slide 8
3
Creating the Assembly
Individual parts only prove themselves once they're mated together — chassis, standoffs, and the Wombat controller as one file.
1
Mate the printed chassis to a Wombat reference model
Confirms bolt-hole alignment and port clearance before anything hits the printer.
2
Add coincident and distance mates for every fastener
Catches interference that a single-part sketch would never reveal.
3
Motion-check the assembly
Drag components through their expected range — wheels, arms, cable runs — to confirm nothing collides.
4
Save the assembly as the source of truth
Every later revision edits this file, not a disconnected single part.
8

## Slide 9
4
From Solid Model to Printable G-Code
A slicer turns the SolidWorks assembly's exported part into layers, paths, and print settings the printer can actually follow.
Export STEP / STL
Each finalized part leaves SolidWorks as a mesh, ready for slicing software.
Orient & support
Choose the print orientation that avoids overhangs on load-bearing faces.
Set walls & infill
Chassis parts get denser infill where the Wombat's weight actually sits.
Preview the layers
Walk through the simulated print before committing filament and time.
9

## Slide 10
4
OrcaSlicer and Cura, Side by Side
We keep both installed — different parts benefit from different strengths.
OrcaSlicer
Cura
Best for
Precision structural parts (chassis, mounts)
Quick classroom prints, broad printer support
Calibration tools
Built-in flow, pressure-advance & tolerance tests
Basic profiles; less built-in tuning
Support strategy
Fine-grained tree & organic supports
Reliable, simpler support structures
Team familiarity
Preferred once students want finer control
Easiest on-ramp for new team members
10

## Slide 11
5
Print, Then Meet Over the Part
On the print bed
Print the chassis exactly as sliced — no last-minute manual edits.
Bring both robots' copies to the table for a fair side-by-side.
Fit-check against the real Wombat controller and drivetrain, not just the CAD assembly.
At the review meeting
Every team member gets to handle the print and flag a concern before it's dismissed.
Decisions are written down: what changes, who owns the CAD edit, by when.
A part is only 'done' once the whole team agrees it solves the original LEGO-stage problem.
11

## Slide 12
6
Closing the Loop: Iterate
Every review meeting feeds directly back into the SolidWorks assembly — not a new file, the same one, revised.
Edit CAD
Re-slice
Re-print
Re-review
Log changes
What we track between revisions
Version-numbered CAD files, one line per change in a shared log.
Which physical print each revision fixed, tied back to a specific review note.
Whether the fix still matches the original LEGO-stage constraints — or if those constraints changed too.
STL exports kept alongside each locked revision for competition documentation.
12

## Slide 13
The Full Cycle, Revisited
LEGO Build
Physical fit & spatial reasoning
→
SolidWorks
Precision from a real reference
→
Assembly
Mate parts, catch interference
→
Slice
OrcaSlicer or Cura, by the job
→
Print
One truth: what's on the bed
→
Review
Whole team, written decisions
↺
Loop back to “LEGO Build” only when the fix changes physical fit; otherwise revisions re-enter at SolidWorks.
13

## Slide 14
Takeaways for Your Own Classroom
Don't skip the LEGO stage
It's the cheapest, fastest design review your students will ever get.
Two slicers isn't overhead, it's leverage
Match the tool to the part instead of forcing one workflow on everything.
Make the review meeting mandatory
The workflow only closes the loop if revisions are actually discussed, not just reprinted.
Start from vetted geometry
Team Home Base STL files save hours and keep dimensions honest for documentation.
14

## Slide 15
Questions & Discussion
Roger Clement
rclement@nobleps.com • KIPR Robotics Education