## Slide 1
THE GYRO
IN A NUTSHELL
Bias, theta, and the theory that makes both worth knowing
Roger Clement • KIPR Robotics Education

## Slide 2
It Measures Speed, Not Angle
gyro_z() returns angular velocity — how fast the robot is turning right now, not how far it has turned.
The raw signal
A stationary sensor should read zero degrees/second.
Turning faster produces a bigger reading, in either direction.
That reading is a rate — angle only appears once you accumulate it over time.
The one-line theory
angle = ∫ (angular velocity) dt
In code, that integral is just a running sum, sampled every loop:
theta += gyro_z() - bias;
// runs once per control-loop tick
2

## Slide 3
Bias: the Zero That Isn't Quite Zero
Every gyro has a small, constant offset baked into its “at rest” reading — bias is how you measure and remove it.
compute_bias(int samples) {
long total = 0;
for (i = 0; i < samples; i++) {
total += gyro_z();
msleep(5);
}
return total / samples;
}
Robot sits motionless; average several readings to cancel out sensor noise.
Why it matters
Skip bias, and a “straight” drive slowly curves — the offset accumulates every single loop tick.
Bias has no dependency on distance or ticks, so it's always calibrated first, before anything else.
Recalibrate per run: temperature and orientation can shift bias slightly between matches.
3

## Slide 4
Theta: the Running Memory of Heading
theta is the accumulated turn since a drive or turn began — the whole reason bias-corrected readings are worth summing.
1
Start at zero
theta = 0 the moment a maneuver begins — it only tracks drift since then, not absolute compass heading.
2
Add the bias-corrected rate each tick
theta += gyro_z() - bias; every loop, so small errors are caught before they compound.
3
Turn theta into a steering correction
correction = (speed * theta) / 12000; nudges one wheel faster, one slower, proportional to how far off-heading the robot has drifted.
4
Reset it at the next maneuver
A fresh drive() or turn() call starts theta over — it isn't a global position, just a local heading memory.
4

## Slide 5
Putting It Together
Two calibration steps, one running variable, and a straight line stays straight.
Calibrate bias
Sit still, average gyro_z() to find the true zero.
→
Read the rate
Every loop tick, sample gyro_z() minus bias.
→
Accumulate theta
Sum the corrected rate into a running heading drift.
→
Correct and repeat
Steer proportional to theta; reset theta on the next maneuver.
Skip the order — TPI before bias, or drive before either — and every downstream number inherits the error.